## Slide 1
Sampling
Physio-chemical characterisation of two AMD sites in Mpumalanga
Identification of parameters in excess of legislative limits
and health effects of exposure
Critical evaluation of the chemical composition of acid mine drainage for the development of statistical correlations linking electrical conductivity with acid mine drainage concentrations
Electrical conductivity used as proxy to predict parameter concentrations in AMD, and regression equations used to derive electrical conductivity values corresponding to water quality limits for predicted parameters
Seasonal variance and
correlation between parameters identified.
Regression analysis
Best fit regression lines selected and outliers statistically rejected
TDS = 5.9804x
TA = 0.0127x1.6623
Dissolved S = 1.1498x
Dissolved Fe = 0.000006x2.4675
Regression equations for prediction of TDS, total acidity, dissolved sulfur, and iron concentrations using EC value (mS/m)
Regression equations used to derive EC values corresponding to predicted parameter compliance limits for a rapid test to trigger further analysis and appropriate remedial action
EC ≈ 201 mS/m ≈ TDS -1200 mg/L limit
TA – No allocated compliance limits
EC ≈ 72 mS/m ≈ Dissolved S ‒ 83 mg/L acute health limit
EC ≈ 173 mS/m ≈ Dissolved Fe ‒ 2 mg/L chronic health limit